## Slide 1: Sonar Propagation Modeling in Spherical-Time Coordinates
Theory and Verification Tests
Sean Reilly – August 2011

## Slide 2: Acknowledgements
This paper was developed as part of Sean Reilly’s PhD studies at the Ocean Engineering Department of the University of Rhode Island, under the direction of Dr. Gopu Potty and Dr. James Miller.
Parts of this effort have also been funded by the High Fidelity Active Sonar Training (HiFAST) Project at the U.S. Office of Naval Research, and internal research and development (IRaD) efforts at Alion Science and Technology, Inc.
The theory for reflection from a 3–D slope was developed by Dr. Michael Goodrich (Alion), who also made significant contributions to the development of test cases for this model.

## Slide 3: Objectives
Create a much faster TL model for real-time, littoral, active sonar sim/stims by revisiting fundamental assumptions of ray theory.
Speed goals:
  100 targets for one sensor
  Update rates faster than the speed of sound
  On a single core of an average laptop
  Insignificant loss in accuracy at MF and HF freqs.
  Then, once we have a fast algorithm, expand to additional sensors using better hardware.
Foundation for very fast bistatic reverberation model.

## Slide 4: Approach
3-D spherical coordinates (lat, long, alt)
  Avoids translation of environmental data into 2-DxN.
Time domain ray trace
  Improves continuity of wavefront with fewer rays.
  Works best at mid and high frequencies.
Hybrid Gaussian beams
  Improves performance in shadow zones and at lower frequencies.
Test using publicly available databases.
  Add Navy databases later as extensions of class hierarchy.

## Slide 5: Theory
The math behind the model

## Slide 6: Rays in Time Domain
1) eikonal
2) use rays along paths
3) use
4) use
Coupled vector ODEs in 3-D
Solved using initial conditions & marching solution
this model
typical ray model

## Slide 7: Rays in Spherical Coordinates
latitude
= p/2-q
altitude = h
r = R + h
R
equator
Earth’s axis
center of
the earth
center of
curvature
area of operations
longitude = f
use WGS-84 ellipsoid, but assume uniform curvature over area of operations

## Slide 8: Adams-Bashforth 3 Integrator
Estimates next time step from explicit terms in previous three.
  Implement as a cached circular queue of 4 wavefronts.
  Single calculation of sound speed and derivative (slowest calculations) per iteration.
  Single calculation of sin q and cot q per iteration.
AB3 is as accurate and much faster than Runge-Kutta 3, but not self starting.
tn+1
tn
tn-1
tn-2
tn+2
wavefront

## Slide 9: Hybrid Gaussian Beam TL
Use spreading to estimate divergence instead of dynamic ray equations.
Form 2-D Gaussian beams that are centered between rays. Time domain wavefront keeps contributions in phase.
Treat Wienberg/Keenan factor as spreading part of overlap-add process
Avoids normalization problems of Cerveny approach.
Gaussian
beam centers
eigenray
target

j+1

j



k

j+2

j
-
1



k+1



k+2



k
-
1
Launch D/E
Launch AZ
2w
j+1
peak  1/width
View across wavefront

## Slide 10: Under Sea Modeling Lib (USML)
Fundamental Data Types
Data Grids
Sequences
World Coordinates
uBLAS Extensions
abs, arg, sqrt, max, ...
cos, acos, cosh, acosh, ...
exp, log, pow, ...
NetCDF Files
Bathymetry
Ocean Profiles
COARDS, WOA, ETOPO
Ocean Components
Profiles
Attenuation
Boundaries
Reflection Loss
Gaussian Rays
Wave Fronts
Eigenray Results
ProplosS Results
uses
acoustic
models
modeling
framework
Focused on speed, ease of integration, and ease of extension.
Test driven development process

## Slide 11: Vectorization
Implement wavefront propagation in vector form
  Wavefronts step through the environment as a unit.
  Unfortunately, many parts of interface collision and eigenray estimation process can’t be vectorized yet.
Employ uBLAS as a Matlab-like processing foundation
  Widely used C++ matrix/vector library based on expression templates.
  Eliminates key obstacles to efficient numerical computing in C++, namely temporaries and virtual function calls.
  Unwraps matrix/vector operations to avoid branching.
  Significantly faster then Blitz++, POOMA, MTL.
ViennaCL extension implements uBLAS on GPUs.
  Thought still needed to minimize data transfers between CPU and GPUs.
References:
T. Veldhuizen, "Expression Templates," C++ Report, Vol. 7 No. 5 June 1995, pp. 26-31
http://en.wikipedia.org/wiki/Expression_templates
http://www.boost.org/doc/libs/1_46_1/libs/numeric/ublas/doc/index.htm

## Slide 12: Verification Testing
Do theory and implementation work as designed?

## Slide 13: Refraction Tests
Time step
10 msec
100 msec (1:50)
Path type
rhumb lines
model
Great Circle Routes
Munk Profile
Max deviation from great circle routes is 2.81x10-10 degrees over 1500 km distance.
No evidence of false caustics,
even using 100 msec time step.
Error measure needs analytic solution.
100 msec time step
Afraid of earth radius factors?

## Slide 14: Reflection Testing
Analytic Slope
Malta Escarpment ETOPO2
Ray D/E increases by twice the slope
to within 10-5 deg maximum deviation.
Reflection from realistic bottom
causes out of plane paths.
top view
50 msec time step
side view
1 msec time step
to measure angles
downslope
18 nmi offset
Impact of bottom reflections?

## Slide 15: Lloyd’s Mirror TL Testing
rms difference = 0.1145 dB
r2 correlation = 87.08 %
Most mismatch at ranges
within the first few time steps.
rms difference = 0.3122 dB
r2 correlation = 90.71 %
Gaussian beams not quite at
full strength near interface.
50 msec time step
50 msec time step
Hybrid Gaussian beams correct?

## Slide 16: N2 Linear TL Testing
Source Depth = 66.7 yds
Receiver Depth = 66.7 yds
Frequency = 2000 Hz
c0 = 1677.3319 yd/sec
g0 = 1.2286762 sec-1
ref: M. A. Pedersen, D. F. Gordon, "Normal-Mode and Ray Theory Applied to Underwater Acoustic conditions of Extreme Downward Refraction", J. Acoust. Soc. Am. 51 (1B), 323-368 (June 1972).
Hybrid Gaussian beams
correct near shadow zone?

## Slide 17: Future: Fast Bistatic Reverberation Model
Generate interface eigenrays as a side-effect of wavefront reflection (separate thread).
Gather source eigenrays as a function of ts, js, s.
Interpolate source eigenrays as function of q, f.
For each receiver
  Gather receiver eigenrays as a function of tr, jr, r.
  For each r and s
    Lookup ts, js at each q(tr, jr), f(tr, jr).
    Lookup source eigenrays and beam pattern at ts, js
    Combine source and receiver eigenrays to compute A Bs Br K product
    Use uneven grid of t = tr + ts to generate gridded Rrs(t).
  Sum Rrs(t) over r and s.
t = travel time
j = launch azimuth
s = source path #
r = receiver path #
q = co-latitude
Io=source level
L = transmission loss
B = beam pattern
K = scattering kernel
f = longitude

## Slide 18: Conclusions
Positive comparisons to TL benchmarks.  so far
  Strongly suggests that the theory derivation is OK.
  Test driven development process means that each USML software component has been extensively tested.
Much faster than current models?  still un-proven
  But poised for transition to GPU architecture.
Short term goal  publish in peer-review literature
  Use an open, established, peer-reviewed process that maximizes input from the scientific community.
  Theory paper is almost ready for submission. JASA? JCA?
  Verification testing paper is in the works.
  Validation testing paper sometime after that.